Magura rim brake

Brake pad travel test

5/3/09

| Brake lever model | Lever blade | Piston size | Brake pad distance (both sides added together) | Notes |
| --- | --- | --- | --- | --- |
| HS24 | Stock alloy, no TPA knob | 16mm | 14.30 mm | Lever contacted handlebar and prevented piston from being driven to true bottom of stroke |
| HS22 | Stock alloy long lever, no TPA knob | 16mm | 13.16 mm | Long lever blade hits the handlebar before piston is driven to bottom of the stroke. |
| HS22 | Stock alloy long lever, no TPA knob | 16 mm | 17.54 mm | Slid lever body down to end of handlebar so the lever blade wouldn’t strike handlebar and piston can be driven to true bottom of stroke. See picture #1 of lever blade at extreme angle |
| HS22 | Modified (pre 2005) HS33 blade with red TPA knob | 16 mm | 14.37 mm | TPA left all the way out. Lever blade hits handlebar very close to the bottom of piston stroke. See picture #2 |
| HS22 | Modified (pre 2005) HS33 blade with red TPA knob | 16mm | 14.97 mm | PTA knob adjusted so the lever blade stays just out of contact with the handlebar when the lever won’t drive piston any further down |
| HS33 (pre 2005) | Stock alloy with red TPA knob | 14mm | 10.03 mm | TPA knob left all the way out. |
| HS33 (post 2005) | NA | NA | NA | Post 2005 lever not available for testing at this time. |

All tests used the same late model lightly used wheel cylinders, the same 18” brake line and the entire brake assembly was bled with Magura red blood after each lever body change and tested for leaks.

All measurements were taken with the same digital caliper. See pictures #3 and #4